Manual on Standard Operating Procedures (SOP’s) and Critical Control Points for Gari Processing

Outline

- Objective of Gari processing

- Important activities for Gari processing

- Materials needed

- Standard Operating Procedures and Critical Control Points

Objective of Gari processing

- To determine the percentage Gari Quantity

Important activities for Gari processing

-  Weighing the roots, Peeling, Mashing, Pressing, Pulverizing and Frying

Materials needed

- Tablet or mobile phones for data capture using fieldbook, Cutler, Knifes, Weighing Scales, Sacks, Crate, polythene bags, Bowls, ribbons, grating machine, tray, plastic buckets, pressing jack, frying machine, markers, plastic container, barcode sticky labels

Standard Operating Procedures and Critical Control Points for setting up field trials

| s/n | Standard Operating Procedures | Critical Control Points |
| --- | --- | --- |
| 1 | State objectives of process clearly | Purpose for the processing must be known to team members |
| 2 | Identify the Processing team and assemble all necessary materials using the checklist | Ensure all equipment are functioning properly |
| 3 | Weighing the selected roots from individual plots (20kgs /10kgs of uniform large roots) | Ensure that the scale properly calibrated, Ensure removal of foreign bodies (sand and dirt) from samples before weighing |
| 4 | Peeling of weighed roots | Ensure that all the peels are inside the crate |
| 5 | Weighing of peels and peeled root | Ensure that the scale properly calibrated, clear instructions to be given to remove nylon/sack weight for measuring peels/peeled root |
| 6 | Wash the root thoroughly | After washing make sure it is well labeled |
| 7 | Grate the cleaned roots using Grating machine | Ensure that Grating machine is working properly, and tray is underneath for collecting. Clean the machine after each sample. |
| 8 | Weighing the grated mash | Ensure that the scale properly calibrated |
| 9 | Grated sample is left for fermentation for 3 days | Ensure you have enough buckets for performing this task and label the buckets |
| 10 | Fermented sample is pressed using pressing machine for 24 hrs. to dewater | Ensure pressing machine is working properly and sack are in good condition to avoid leaks |
| 11 | Weighing the pressed sample | Ensure that the scale properly calibrated |
| 12 | Pressed sample should be pulverized using grating machine | Ensure that Grating machine is working properly, and tray is underneath for collecting. Clean the machine after each sample. |
| 13 | Weighing the pulverized sample | Ensure that the scale properly calibrated |
| 14 | Fry the pulverized sample on frying machine until the sample is complete dry. (usually takes from 5 to 20 min) | Ensure that Frying machine is working properly, and frying is done uniformly. |
| 13 | Sieve the fried sample using two sizes of Sieve | Separate the coarse and medium from fine granules |
| 14 | Weighing the coarse, medium and fine granules. | Ensure that the scale properly calibrated |
| 15 | Fine granule weight is your Dry Gari weight | Availability of enough vehicles and skillful personnel to convey planting materials to the field |
| 16 | Generate sticky Barcode labels from cassavabase and stick them to each sample in separator container | Ensure the availability of labels |
| 17 | Store these containers for further processing of Gari and Eba sensory | Ensure they stored in a clean and safe please and each sample is well covered. |

Images for Gari Processing:

Fresh samples           Weighing sample   20kg of sample     Peeled root            Peels of the roots

Weighing peel        Weighing peeled roots   Washed roots     Grated roots               Fermenting

Dewatering                Pulverizing           Frying                     Sieving                  Fine gari